## Slide 1: Advanced FTC Code
Don’t panic!
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 2: Intro
Things covered in this class:
  Andriod Studio
  Gyro
  Driving Straight
  Pathfinding

## Slide 3: Andriod Studio
A lot more complicated than OnBoard Java
A lot more flexible as well.
A good tool to know

## Slide 4: Android Studio Setup
Download/Install JDK
Download/Install Android Studio
Get FTC project (next screen)
Import the FTC project.
Hit yes to installing all of the tools and updates Android Studio needs

## Slide 5: FTC Project
Github has it.
https://github.com/ftctechnh/ftc_app
You can download and use it from Github.
Better to fork the code into your Github project. This lets your team check in code,

## Slide 6: Gyro
The gyro on the Rev Expansion Hub is a BNO055IMU. It’s Adafruit’s gyro.
Other gyro major gyro is MPU-9250, it’s Sparkfun’s gyro.
There are trade off. The biggest pro for the BNO is, the code is already written.

## Slide 7: Gyro Setup
BNO055IMU.Parameters parameters = new BNO055IMU.Parameters();
parameters.angleUnit = BNO055IMU.AngleUnit.DEGREES;
parameters.accelUnit=BNO055IMU.AccelUnit.METERS_PERSEC_PERSEC;
parameters.calibrationDataFile = "BNO055IMUCalibration.json";
parameters.loggingEnabled = true;
parameters.loggingTag = "IMU";
parameters.accelerationIntegrationAlgorithm = new JustLoggingAccelerationIntegrator();

## Slide 8: Gyro Setup
imu = hardwareMap.get(BNO055IMU.class, "imu");
imu.initialize(parameters);
imu.startAccelerationIntegration(new Position(), new Velocity(), 1000);

## Slide 9: Gyro get data
telemetry.addAction(new Runnable()
{ @Override public void run()
{
angles = imu.getAngularOrientation(AxesReference.INTRINSIC, AxesOrder.ZYX, AngleUnit.DEGREES); gravity = imu.getGravity();
}
});

## Slide 10: Gyro get data
telemetry.addLine().addData("heading", new Func<String>()
{ @Override public String value() { return formatAngle(angles.angleUnit, angles.firstAngle); }
});

## Slide 11: Driving Straight
FTC robots for the most part drive straight.
The field is not that big.
Gyro is used for Tele/Auto.

## Slide 12: Driving Straight
FTC robots for the most part drive straight.
The field is not that big.
Gyro is used for Tele/Auto.

## Slide 13: Fast and Slow Buttons
double y = driveJoystick.getRawAxis(1); double x = driveJoystick.getRawAxis(2);
x = DriveMath.DeadBand(x,0.05); y = DriveMath.DeadBand(y,0.05);
if (false == driveJoystick.getRawButton(Constants.kFastButton)) {
} else {
if (false == driveJoystick.getRawButton(Constants.kSlowButton)) {
y *= Constants.kNormalSpeed; x *= Constants.kNormalTurnSpeed;
} else {
y *= Constants.kSlowSpeed; x *= Constants.kSlowTurnSpeed;
}
}

## Slide 14: Add the Gyro / Turning
turn = x; speed = y;
mCurrentAngle = angles.firstAngle
if (Math.abs(turn) > 0.2) {
RawDriveRobot(speed*.5, turn*.5);
mTargetAngle = mCurrentAngle;
} else {
* Next page *
}

## Slide 15: Straight and stop
if (Math.abs(speed) > 0.1) {
double angleError = (mTargetAngle - mCurrentAngle);
turnThrottle = angleError * kPgain - (currentAngularRate) * kDgain;
double maxThrot = DriveMath.MaxCorrection(speed, kMaxCorrectionRatio);
turnThrottle = -1*DriveMath.Cap(turnThrottle, maxThrot);
RawDriveRobot(speed,turnThrottle);
}
else
{
RawDriveRobot(0, 0); mTargetAngle = mCurrentAngle;
}

## Slide 16: Raw Drive the Robot
if(mActualSpeed != speed) {
if(mActualSpeed<speed) {
mActualSpeed = Math.min(mActualSpeed+kSpeedGain, speed);
}
else {
mActualSpeed = Math.max(mActualSpeed-kSpeedGain, speed);
} }
double targetSpeedL = (mActualSpeed + turn);
double targetSpeedR = (mActualSpeed - turn);
DriveLF.set(targetSpeedL); DriveRF.set(targetSpeedR);

## Slide 17: Jaci’s Pathfinding
The most populare pathfinding in FRC.
Jaci is on Chiefdelphi’s board all the time.
She loves fixing and making it better.

## Slide 18: Jaci’s Pathfinding
Unfortunately it’s written in C++
I’ve taken the C++ and wrote a tool in Visual Studio to take in a path.csv file an put out a path in java.
It’s in the Github project below.

## Slide 19: Jaci’s Pathfinding
Unfortunately it’s written in C++
I’ve taken the C++ and wrote a tool in Visual Studio to take in a path.csv file an put out a path in java.