## Slide 1: Advanced FTC Code
Jim Wright 2017

## Slide 2: Intro
Things covered in this class:
  New things
  StopWatch class
  I2C stuff
  PID review

## Slide 3: OnBot connection.
This was new to Jim, I’m not sure it was here last year.
You will enable another WIFI connection to the Robot Controller
Use the Program and Manage menu item.
From this panel you will see the WIFI name and WIFI key for the robot controller

## Slide 4: Block and OnBot connection.
You will enable another WIFI connection to the Robot Controller
Use the Program and Manage menu item.
From this panel you will see the WIFI name and WIFI key for the robot controller.
Point your browser to the IP address on the RC. Something like:
http://192.168.49.1:8080

## Slide 5: OnBot
@TeleOp(name="OnBotTele", group="Linear Opmode")
// @Autonomous(...) is the other common choice
public class OnBotTele extends LinearOpMode {
rightMotor = hardwareMap.dcMotor.get("Right");
waitForStart();
runtime.reset();

## Slide 6: OnBot
while (opModeIsActive()) {
Integer rightEnc = rightMotor.getCurrentPosition();
telemetry.addData("Status", "Run Time: " + runtime.toString());
telemetry.addData("R Enocder", rightEnc.toString());
telemetry.update();
leftMotor.setPower(-gamepad1.left_stick_y);
rightMotor.setPower(-gamepad1.right_stick_y);

## Slide 7: Color Sensor
Run the Color Sensor Example

## Slide 8: StopWatch
A StopWatch is a very useful thing in embedded programming.
You really don’t want to block anything with waits.
Keep the code flowing.

## Slide 9: StopWatch
package org.firstinspires.ftc.teamcode;
public class StopWatch {
long mLastTime = 0;
int mWaitTime = 0;
public StopWatch(int waitTime) {
mWaitTime = waitTime;
}

## Slide 10: StopWatch
public void setTime(int waitTime) {
mWaitTime = waitTime;
}
public boolean isExpired() {
if ((System.currentTimeMillis() - mLastTime) > mWaitTime) {
return true;
}
return false;
}

## Slide 11: StopWatch
public void reset() {
mLastTime = System.currentTimeMillis();
}

## Slide 12: Stop watch example
You have a servo that you want to wait four seconds, then turn the server 180 degrees, for two seconds, then turn it back.
Two StopWatches, one set to 4000ms, the over to 2000ms.

## Slide 13: StopWatch Example
servoStopWatch = new StopWatch(2000);
waitStopWatch = new StopWatch(3000);
servo.setPosition(MIN_POS);
// Wait for the start button
waitForStart();
waitStopWatch.reset();

## Slide 14: StopWatch Example
while(opModeIsActive()){
if(waitStopWatch.isExpired()) {
servo.setPosition(MAX_POS);
if(servoStopWatch.isExpired()) {
waitStopWatch.reset();
} }
else {
servo.setPosition(MIN_POS);
servoStopWatch.reset();
}
idle(); // Hit this every time through the loop
}

## Slide 15: I2C
I tried to get a ‘non-standard’ I2C device working.
I came very close.
It’s very tough sledding
Boy, most sensors you want to deal with are in the libraries, basically stay with them.

## Slide 16: PID Review
requestedGyro = 0;
error = requestedGyro – Kalman(ReadGyro());
acumError += error;
deriv = error - lastError;
lastError = error;
gyroPower = error * Kp + deriv * Kd + acumError * Ki;
leftMotorPower += gyroPower * Kg;
rightMotorPower -= gyroPower * Kg;

## Slide 17: Give me a ‘P’
The P stands for Proportional.
The most important of the control params
error = requestedTicks - countTicks;
motorPower = error * Kp;
Could be requestedResistance if we are using a potentiometer

## Slide 18: Give me a ‘D’
The D stands for Derivative.
The second most important
Sometimes people just use a PD loop.
deriv = error - lastError;
motorPower = error * Kp + deriv * Kd;

## Slide 19: Give me an ‘I’
The I stands for Integral.
Do not make this too big
A bit tricky to tune you have to know your system.
Make sure Requested Ticks can be met or else evil happens.
acumError += error;
motorPower = error * Kp + deriv * Kd + acumError * Ki;