## Slide 1: The Lawfirm of Kalman and Pid
Two Algorithms for controlling robots

## Slide 2: You, the audience
I only get one hour with you
A lot of you know Java
A lot of you know the Control System, if not October 15th all day at the Field House
I want more higher control in our autonomous

## Slide 3: The Gyro is your friend
The gyro keeps your robot going straight.
Hard to turn
You need a gain on the gyro control to turn.
You can also use it as a rough compass.

## Slide 4: The Gyro is your Enemy
The gyro is noisy
The gyro is noisy
Whoa! The gyro is noisy
It also ‘drifts’ however, for us the drift does not need to be taken into account

## Slide 5: Hooking a Gyro up
Find the gyro you want to use:
  SparkFun IMU Breakout - MPU-9250
  Adafruit 9-DOF IMU Breakout - L3GD20H + LSM303
Both have example code from the Web Sites.
Both use I2C.

## Slide 6: Raw Gyro

## Slide 7: The Running average
Average you add up all the numbers and divide by the count.
Take reading every 5ms 30000 counts is a lot of data to keep.

## Slide 8: The Running average
Take the average you have.
Multiply that average by 31/32
Take the new reading and multiply that by 1/32
Add those together.

## Slide 9: Running Average

## Slide 10: That is not that great either
We need a better filter.

## Slide 11: Kalman filter
There are a lot of implementations of the Kalman filter on the internet.
Treat it as a black box, send data into it and get data out of it.
You need to tune it, this is where the real problem is.

## Slide 12: Kalman filter
Depending on the implementation you send in different things.
The one I found you pass in, qAngle, qBias, rMeasure.
I really have not idea of what those mean. Next year I will.

## Slide 13: Badly Tuned KAlman

## Slide 14: Tuning the Kalman filter
I just change the initial inputs until things work
I’m using .1, 1.015, .001
I’m also using the LSM9DS0 gyro.

## Slide 15: WELL Tuned KAlman
LSM9DS0

## Slide 16: PID
The cornerstone of the control algorithms.

## Slide 17: Give me a ‘P’
The P stands for Proportional.
The most important of the control params
error = requestedTicks - countTicks;
motorPower = error * Kp;
Could be requestedResistance if we are using a potentiometer

## Slide 18: Give me a ‘D’
The D stands for Derivative.
The second most important
Sometimes people just use a PD loop.
deriv = error - lastError;
motorPower = error * Kp + deriv * Kd;

## Slide 19: Give me aN ‘I’
The I stands for Integral.
Do not make this too big
A bit tricky to tune you have to know your system.
Make sure Requested Ticks can be met or else evil happens.
acumError += error;
motorPower = error * Kp + deriv * Kd + acumError * Ki;

## Slide 20: Constants too low
LSM9DS0

## Slide 21: WELL Tuned PID

## Slide 22: PID Hitting friction

## Slide 23: Ki is bigger than kp

## Slide 24: Putting them together
requestedGyro = 0;
error = requestedGyro – Kalman(ReadGyro());
acumError += error;
deriv = error - lastError;
lastError = error;
gyroPower = error * Kp + deriv * Kd + acumError * Ki;
leftMotorPower += gyroPower * Kg;
rightMotorPower -= gyroPower * Kg;

## Slide 25: Finished
I’m done