## Slide 1: The FRC Electrical System
Jim Wright
STEALTH 4089

## Slide 2: This Workshop is on my Github
https://github.com/JimWright4089/FIRSTWorkshops/FRC/2022
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 3: Basic Electrical Concepts
Three parts to electricity
  Voltage, units Volts
  Current, units Amps
  Resistance, units Ohms
Other things to worry about
  Temperature, units degrees C/F
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 4: Voltage
You can think of wires like full pipes.
Volts are how big the pipe is (the cross area).
We have two volt “busses”
  12V is the main “bus”, almost everything is 12V
  5V is the logic “bus”, this is offboard computing.
Running a 5V device on the 12V will blow the device up.
Running a 12V device on the 5V will not turn the thing on.

## Slide 5: Current
Current is how hard the pressure is in the pipe.
The end of the pipe where the water goes in is called the “source”
The end of the pipe where the water flows out is the “sink”
In electronics the electrons are actually pulled through the wire.
Circuit Breakers are rated in Amps.

## Slide 6: Resistance
We tend to not worry about resistance in FRC.
The resistance is why the “sink” needs the amount of Amps.
The item that causes the resistance is called a ‘load’
Motors are an example of a ‘load’. If a wheel on a motor is spinning on flat ground it will pull X amps.
If the wheel climbs a ramp, the amps will rise.
You ALWAYS need resistance in a circuit.

## Slide 7: Drawing a load on an electrical schematic

## Slide 8: A bad drawing of a electrical schematic
A battery without a resistance, is called depending how many volts the battery is:
  Short circuit
  A Short
  A Dead Short

## Slide 9: Amp/Hours
The amount of capacity of a battery is measured in Amp/Hours.
Our FRC battery is 18 Amp/hours.
If we have a 1 Amp load, we can run that for 18 hours.

## Slide 10: Ground and Positive
Out of the battery there are two connections
The Positive connection is the “source” of the electricity.
The negative connection is the “sink”, and is called the ground.
The ground is where to volts measure zero.
Like physical work, if a mass is above the ground it have potential energy.
If the mass is on the ground it has zero potential energy.

## Slide 11: Circuit Breakers and fuses
Circuit breakers prevent sorts.
They have an amp rating
If you pull more amps than the rating the circuit breaker opens and stops the flow of amps.
The breakers are temperature sensitive.
Every one we will use is “slow acting” which means that if you pull 41 amps through a 40 amp breaker, it will take a long time to open.
If you pull 80 amps through a 40 amp breaker, it will open quite fast.

## Slide 12: The Primary Distribution System
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 13: The Primary Distribution System
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 14: The Primary Distribution System
Gets the power from the battery to the Distribution Thingys.
The Battery is a 12V 18Amp/Hour. When fully charged its 14V, and while the robot is heavy driving can drop down to 10V.
The main breaker is a 120Amp slow acting breaker, which means it can handle short spikes above 120A.
We want the battery to be at 14-13V at the start of the match.
We can use either 6 gage or 4 gage wire. 4089 uses 6 gage.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 15: Regulated Secondary Power System
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 16: Regulated Secondary Power System
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 17: Regulated Secondary Power System
The distribution boards have a 12V regulator on them, that even if the main battery power goes under 12V, the regulators will put out 12V power.
The fuse ports on the distribution boards can only connect to these devices.
Extra Voltage Regulator Modules (VRM) and Pneumatics Modules can be added but only to the Non-Regulated ports.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 18: Secondary Power System
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 19: Secondary Power System
Mostly Motor Drivers.
Other things like LimeLights.
Circuit Breakers 5Amp, 10Amp, 20Amp, 30Amp, and 40Amp.
We need to look at each load to figure out the right breaker to use.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 20: Minimum Wire Gages.
40Amp breakers need to have 12 gage wires.
30Amp breakers 14 gage wires
20Amp, and all he regulated devices (other than RoboRio) need 18 gage wires.
10Amp, 5Amp, RoboRio, any extra regulated devices 22 gage.
Sensor wires can be 28Amp.
All of these will use Red for positive, Black for ground.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 21: 5V bus
Arduinos and Raspberry Pis need to run on the 5V bus.
Sources:
  Two 1Amp ports on the Voltage Regulator Modules.
  Two .250 Amp ports on the VRM as well.
  Pololu 15 Amp Step down module.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 22: Connecting it into a FRC robot The Rules/Pro Tip
R624
  All non-SIGNAL LEVEL wiring with a constant polarity (i.e., except for outputs of relay modules, motor controllers, or sensors) shall be color-coded along their entire length from the manufacturer as follows:
    A. red, yellow, white, brown, or black-with-stripe on the positive (e.g. +24VDC, +12VDC, +5VDC, etc.) connections
    B. black or blue for the common or negative side (-) of the connectionsBasically, the RoboRio MUST controls ALL actuators (even servos).
My company (Astronics) has a unwritten rule that, all Aircraft Power (28Volt usually) is Red/Black. All 5V power is Orange/Black so they don’t mix.
I would suggest Yellow/Blue for your 5V power bus.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 23: Connecting it into a FRC robot 5V Power Bus
Anderson Quick Connects come in other colors than Red/Black.
  https://powerwerx.com/anderson-powerpole-colored-housings
Anderson Quick Connect Bus
  https://powerwerx.com/8-position-powerpole-distribution-block
Terminal Blocks
  From McMaster or most local Hardware Stores
  McLendon Hardware has a good selection
Termal Block Jumpers
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 24: Wire Connectors
We would like to use Anderson Powerpole connectors.
We also want to connect each load to the same distribution port if we have to rewire the robot at some point.
Every port will have a certain color pattern.
The load will have the same pattern so people have a visual clue what goes where.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 25: Connecting it into a FRC robot TE Con Deutsch Connectors
Digikey sells the best selection
Part Numbers for the 6 pin.
  DT04-6P – Socket Shell
  W6P – Wedge Lock
  DT06-6S – Plug Shell
  W6S – Other Wedge Lock
  0462-201-16141 Socket Pin
  0460-202-16141 Pin
Crimp tool is expensive on Digikey. Cheaper one:
  https://www.customconnectorkits.com/902-499/
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 26: CAN bus
The CAN bus starts at the RoboRio and ends at the Distibution Board.
Motor Drivers and the Pneumatic devices are connected to the bus in between.
The CAN bus has a high wire (yellow), and low wire (green).
They all chain together.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 27: CAN bus
Everything on the bus needs a unique ID
Cross the Road devices are configured with their tool.
Rev Robot devices are configured with the Rev Tool.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 28: Engineering Notebook
The electrical team is responsible to document the following:
  What devises are on with power port.
  What breakers are on each port
  The order of the CAN bus.
  The CAN ID of each devices.
https://github.com/JimWright4089/FIRSTWorkshops