## Slide 1: Offboard Processing (Raspberry Pi and Ardiuno)
Jim Wright
The Whidbey Island Wild Cats 2980

## Slide 2: This Workshop is on my Github
https://github.com/JimWright4089/FIRSTWorkshops/FRC/2022
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 3: This Workshop is on the Web
Workshop:
https://github.com/JimWright4089/FIRSTWorkshops/FRC/2022
Code:
https://github.com/JimWright4089/FIRSTRobots
Web:
https://jimwright.org/robot/robots.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 4: The Workshop Robot Code
The robot in this demo is name the Tornado Platypus
On the code github there are a bunch of sub directories to pay attention to
  TornadoPlatypus
  Arduino
  Feather
  JetsonNano
  RaspberryPi
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 5: The Map!
What is the Hardware
Connecting it into a FRC robot
Standalone Things
WPI Raspberry Pi Image
Ubuntu setup
OpenCV/NTCore/Apriltags
I2C comm to 32bit processor
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 6: What is the Hardware
Raspberry Pi type things (Heavy Processors)
8 Bit processors
32 Bit processors
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 7: Heavy Processors
What are they, how are they used.
Pros:
  Heavy Communication Lifters (WPI Net Tables)
  Heavy Processing
  Mostly Linux
Cons:
  Timers, Linux is bad at LED Strips
  Analog Reading/Writing
  Big, takes lots of power.
  Expensive/Hard to get right now
  Mostly Linux
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 8: Heavy Processors Raspberry Pi type things
Standard Pin out, therefore lots of “hats” for them
Most of them are 5V, draws 2Amps – 5Amps, depending on what you have connected to them.
The pins are 3 volt!!!!!  Oh, so important
They get hot, heatsink cases are needed.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 9: Heavy Processors Raspberry Pis
Raspberry Pi 4 (Rpi4)
  Comes with 1Gb, 2Gb, 4Gb, and 8Gb SRAM
  Micro-HDMI ports
  Lots of documentation on the Web for these.
  Cases are incompatible with Rpi 3, 2, 1
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 10: Heavy Processors Raspberry Pis
Raspberry Pi 3 (Rpi3)
  Comes with 1Gb, 2Gb, 4Gb SRAM
  Full size HDMI ports
  Harder to buy, however, most everyone has one of them lying about.
  Lots of documentation on the Web for these.
  Minimum device for FRC Offboard processing.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 11: Heavy Processors Raspberry Pis
Raspberry Pi Zeros
  Two variants
    Raspberry Pi Zero - Version 1.3
    Raspberry Pi Zero W (Wifi)
  Full size HDMI ports
  No Eithernet port
  One usable USB port, to Usb Hub is needed.
  There power the Limelights (I’ve been told)
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 12: Heavy Processors NVIDIA Jetson Nano
Raw Processing power is between Rpi 3 and Rpi4.
Basically a NVIDIA graphics card strapped to a Rpi
Good for Vision Processing and Machine Learning.
A lot more software expertise is needed to really make ‘em run.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 13: Heavy Processors Jetson AGX Xavier/Orin Nano
AGX Xavier at $1,300 you can’t use it on an FRC Bot
I just include it because this is what Professional Robotics Engineers use.
Orin Nano is just coming out there isn’t a lot of information on it.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 14: Heavy Processors Google Coral Dev Board
Raw Processing power is between Rpi 3 and Rpi4, less than the Jetson Nano.
Good for Machine Learning.
A board built for Tensor Flow
A lot more software expertise is needed to really make ‘em run.
Good enough for Vision Processing
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 15: Heavy Processors UP 4000
Intel Based
Built for Windows IoT
I have one but I’ve not had much time with it.
You can get them reliably now but pricey
12 Volt Based 5Amp!!
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 16: Heavy Processors Limelight
It’s odd to put the Limelight in this section. It really is a Rpi Zero.
Since we are switching from Reflective Tape on the field to Apriltags, I’m guessing teams are working on switching these over.
Most teams own these. So there FREE!!!
I’m hoping for a new firmware release to include the April Tag library.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 17: Jim’s Raspberry Pi 4 favorite cases
Big ‘ol chunk of Alluminum
Fans that use the 5V pins
https://www.adafruit.com/product/4340
Non-fan heat sink cases come in various colors.
The non-fan cases look like they are being discontinued, but I’m not sure if that might be a part-shortage issue.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 18: Arduino type things Both 8bit and 32bit
The concept of an Arduino was game changing in the Embedded world.
  Before Arduino Embedded Engineers had to write low level device drivers from scratch every time.
The Arduino IDE is sooo game changing.
A lot of code is written, and a lot of boards use the IDE.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 19: Arduino type things 8 - bit
The UNO “family” is the most popular.
These are the standard pin outs for 8 – bit processors.
Lot and Lots of “hats” for these.
They are meant for very simple very specific applications.
Not that useful for FRC anymore.
Accepts 5 Volts, pins are 5 Volts.
  This is critical for LED strip applications.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 20: Arduino type things Pololu A-Star 32U4
Pololu A-Star drivers need to be added to the Arduino IDE (more on that later).
I (Jim) considers this the most important FRC off board device.
It’s a Raspberry PI Hat with a UNO built in. So it can source both 5V and 3.3V pins.
The 5V to 3.3V level shifters are built into the I2C lines.
It has a 12V to 5V regulator on it, you can wire it into the PDP/PDH safely
https://www.pololu.com/product/3118
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 21: Arduino type things 32 - bit
These have taken over the small processor space.
They are faster with more RAM and Flash (programming capacity).
Most sensors are now being designed for these.
5V in, however like the Rpis 3.3V pins.
SparkFun's Qwiic Connect plugs are quickly becoming standard and they make wiring thing easy. (These are I2C at the low level)
All processors use the Arduino IDE
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 22: Arduino 32bit type things Adafruit Feather Family
ATSAMD21 Cortex M0
  256KB of FLASH + 32KB of RAM
  48MHz with 3.3V logic/power
ATSAMD51 Cortex M4
  512 KB flash, 192 KB RAM
  120 MHz, 32-bit, 3.3V logic and power
I (Jim) use these for LED matrix drivers.
Adafruit has ‘hats’ for these.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 23: Arduino 32bit type things SparkFun Thing Plus - SAMD51
It’s a M4 processor.
This has the Qwiic connector built in.
I (Jim) use these for driver station buttons.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 24: Arduino 32bit type things SparkFun MicroMod system
Weird idea, any processor wired into a bunch of peripherals.
Easy wire, secure
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 25: The Map!
What is the Hardware
Connecting it into a FRC robot
Standalone Things
WPI Raspberry Pi Image
Ubuntu setup
OpenCV/NTCore/Apriltags
I2C comm to 32bit processor
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 26: Connecting it into a FRC robot The Rules
R503
  With the exception of servos, fans, or motors integral to sensors of COTS computing devices permitted in R501, each actuator must be controlled by a power regulating device. The only power regulating devices for actuators permitted on the ROBOT include:
Basically, the RoboRio MUST controls ALL actuators (even servos).
Off board devices are sensors and LED status/decoration things.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 27: Connecting it into a FRC robot
With the exception of the UP 4000, all of the previous devices take in 5 volts.
The 8bit and 32bit boards can be powered off of the 5V ports of the VRM, or USB ports of the driverstation laptop.
The Heavy Processors however, are creeping above the 2Amp limit of the VRM
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 28: Connecting it into a FRC robot Getting power to ‘em
Pololu has an amazing assortment of 12V to 5V converters.
Pololu 5V, 15A Step-Down Voltage Regulator D24V150F5
  https://www.pololu.com/product/2881
12V lines come from the PDP/PDH
5V lines come out of it
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 29: Connecting it into a FRC robot The Rules/Pro Tip
R624
  All non-SIGNAL LEVEL wiring with a constant polarity (i.e., except for outputs of relay modules, motor controllers, or sensors) shall be color-coded along their entire length from the manufacturer as follows:
    A. red, yellow, white, brown, or black-with-stripe on the positive (e.g. +24VDC, +12VDC, +5VDC, etc.) connections
    B. black or blue for the common or negative side (-) of the connectionsBasically, the RoboRio MUST controls ALL actuators (even servos).
My company (Astronics) has a unwritten rule that, all Aircraft Power (28Volt usually) is Red/Black. All 5V power is Orange/Black so they don’t mix.
I would suggest Yellow/Blue for your 5V power bus.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 30: Connecting it into a FRC robot 5V Power Bus
Anderson Quick Connects come in other colors than Red/Black.
  https://powerwerx.com/anderson-powerpole-colored-housings
Anderson Quick Connect Bus
  https://powerwerx.com/8-position-powerpole-distribution-block
Terminal Blocks
  From McMaster or most local Hardware Stores
  McLendon Hardware has a good selection
Termal Block Jumpers
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 31: Connecting it into a FRC robot TE Con Deutsch Connectors
Digikey sells the best selection
Part Numbers for the 6 pin.
  DT04-6P – Socket Shell
  W6P – Wedge Lock
  DT06-6S – Plug Shell
  W6S – Other Wedge Lock
  0462-201-16141 Socket Pin
  0460-202-16141 Pin
Crimp tool is expensive on Digikey. Cheaper one:
  https://www.customconnectorkits.com/902-499/
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 32: Connecting it into a FRC robot Control System
All the processing needs to go through the RoboRio everything needs to attach to it.
Heavy Processors connect through Ethernet and talk Net Tables (NTCore).
8bit and 32bit could talk I2C, however, the RoboRio I2C port is ‘SUS’
8bit and 32bit can connect to the digital IO or the serial port.
  However, it’s convenient to have the 8bit and 32bit talk to the Heavy Processors and have them talk NTCore
The 32bit processors can talk Ethernet, however, compiling NTCore for them is a problem. If WPI would switch to the MQTT protocol this problem would be solved.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 33: Connecting it into a FRC robot Control System
The Ethernet on the robot is getting crowded.
Adding a switch to the robot is a good idea.
The lightest switch I (Jim) have found is the NETGEAR 5-Port Gigabit Ethernet Unmanaged Switch (GS205) or the non-Gigabit switch (FS205)
It takes 12V power and can be plugged into the VRM
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 34: Connecting it into a FRC robot Control System
Rpi4 with Pololu Hat
12V cables soldered into the power plugs.
The FAN in the case run off 5V so the 5V and ground lines run to the plug.
There is a cable for LED Ring
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 35: Connecting it into a FRC robot Control System
Rpi4 with Qwiic connector on it.
5V supply
This case doesn’t have fans
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 36: Connecting it into a FRC robot Control System
Raspberry Pis take a lot of amps.
If the Pi is not getting enough current it will show it on the display.
Wire your Pi into robot and plug it into a display.
Turn the robot on.
If the Pi is not getting enough current a lightning bolt will appear in the upper right corner.
If it’s there you need to put a bigger power converter on your robot.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 37: The Map!
What is the Hardware
Connecting it into a FRC robot
Standalone Things
WPI Raspberry Pi Image
Ubuntu setup
OpenCV/NTCore/Apriltags
I2C comm to 32bit processor
https://github.com/JimWright4089/FIRSTWorkshops
GET UP AND STRETCH

## Slide 38: The Map!
What is the Hardware
Connecting it into a FRC robot
Standalone Things
WPI Raspberry Pi Image
Ubuntu setup
OpenCV/NTCore/Apriltags
I2C comm to 32bit processor
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 39: Standalone Things Examples
The Whidbey Island Wildcats
  Feather M4 based
  32X64 LED Matrix
Stealth Driver Station Button Board
  Thing Plus - SAMD51
  Arcade Buttons
  Qwiic Encoders
  Adafruit LED Rings
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 40: Standalone Things Arduino IDE
IDE can be found here: https://www.arduino.cc/en/software
At start the IDE only has Arduino boards
On Preferences click on the browse button for the Additional Board Manager
Find the URL on the board makers Web site and add it.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 41: Standalone Things Arduino IDE
There is a Library for almost any device you can buy on Pololu, Sparkfun, or Adafruit.
Under Tools click on manager library and then search for the library
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 42: Standalone Things Arduino IDE
Plug the device in and Windows should recognize it.
Under tools you should be able to select the device you are working with.
Find the Com port in the Device Manager
The select that COM port
Test everything is working using the Blink Example, every board should have the blink LED.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 43: Standalone Things Wildcats Robot Googly Eyes
2980 had a set of googley eyes on their robot.
Feather M4 based
  https://www.adafruit.com/product/3857
32X64 LED Matrix
  https://www.adafruit.com/product/2279
Feather LED Matrix Hat
  https://www.adafruit.com/product/3036
Pololu 12V to 5V stepdown converter
  https://www.pololu.com/product/3782
Code
  https://github.com/JimWright4089/FIRSTRobots/tree/master/Code/Feather/RobotEyes
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 44: The Map!
What is the Hardware
Connecting it into a FRC robot
Standalone Things
WPI Raspberry Pi Image
Ubuntu setup
OpenCV/NTCore/Apriltags
I2C comm to 32bit processor
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 45: WPI Raspberry Pi Image What is it
WPI, maker of the WPI lib we all use have a Raspberry Pi image of the OS with NTCore, Camera Server, OpenCV in a package.
https://github.com/wpilibsuite/WPILibPi/releases
Download the WPILibPi_image-v2022.1.1.zip
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 46: WPI Raspberry Pi Image Buring Flash
The OS for a Rpi is on a SD card.
To build this card use the Raspberry Pi Imaging tool
  https://www.raspberrypi.com/software/
Unzip the zip file, choose custom image in the tool, then plug in a micro SD card (and it’s adaptor) into your computer and select the card.
Hit Write.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 47: WPI Raspberry Pi Image Pi Image Pro Tip
Since SD cards are the hard drives for a Rpi, you can swap them easily.
It becomes hard to figure out which SD card is which image.
On the back of SD cards I paint a little pattern.
I have a Google Docs File of the color pattern and which image it is.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 48: WPI Raspberry Pi Image OS is locked
Plug the SD card into the Pis SD card port.
Connect up an ethernet, webcam, display and keyboard.
On boot up the user is ‘pi’ and password is ‘raspberry’
The prompt will end in a (RO), which indicates the OS is in read only.
Use ‘ifconfig’ to see the IP address.
Type the IP address into a web browser.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 49: WPI Raspberry Pi Image Web Page
The first page is just status, however, at the top of the page are the Read Only/Write buttons.
On the Vision Setting is the box to enter your team number. Set the system to write and hit save.
On this Panel you can see what the camera is seeing.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 50: WPI Raspberry Pi Image SSH
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 51: WPI Raspberry Pi Image Color blob Example
The Application tab of the web page will let you build your OpenCV pipeline.
Download the example from the bottom buttons
I’m a C++ programmer so I will use C++, it is homework for you to figure out Java
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 52: WPI Raspberry Pi Image Color blob Example
Code is located at:
  https://github.com/JimWright4089/FIRSTRobots/tree/master/Code/RaspberryPi/cpp-multiCameraServer
Explanation of the code:
  http://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 53: WPI Raspberry Pi Image Color blob Example
Upload the zip file you just downloaded.
On the command line unzip the file unzip cpp-multiCameraServer.zip.
On the application page upload the file main.c.
On the Rpi the main.c file will appear in the home directory.
Move it to the example directory with
  mv main.cpp ./cpp-multiCameraServer/
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 54: WPI Raspberry Pi Image Color blob Example
If you are building on the Rpi, you need to change the Makefile.
nano Makefile
Change the line:
  CXX=arm-raspbian10-linux-gnueabihf-g++
To
  CXX=g++
Run ‘make’
Run ‘make install’
Run ‘sudo svc -t /service/camera’
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 55: WPI Raspberry Pi Image Color blob Example
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 56: WPI Raspberry Pi Image Color blob Example
If the Rpi is on you desk, put it on the robot, you will not need the Display and Keyboard any more.
Finding the IP address is a bit painful.
  From Command line ssh to the RoboRio ‘ssh admin@10.40.89.2’
  Once you’re in the RoboRio ‘ping wpilibpi’
The IP address should be shown and type that into the browser address.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 57: WPI Raspberry Pi Image Color blob Example
On the Vision Status, you can turn the print statements on and see what is happening.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 58: WPI Raspberry Pi Image Color blob Example
The default dashboard should have two cameras on it.
Processed
Threashold
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 59: The Map!
What is the Hardware
Connecting it into a FRC robot
Standalone Things
WPI Raspberry Pi Image
Ubuntu setup
OpenCV/NTCore/Apriltags
I2C comm to 32bit processor
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 60: Ubuntu setup Raspberry PI Imaging tool
We have seen this tool already.
We need to decide which image to put on.
Ubuntu
  A large amount of help is available. Anything but a Rpi this really is the only thing available.
Raspberrian 64bit for sure
  Lite does not have the desktop.
    If you have used Raspberrian already use this. It’s a it faster since there isn’t a UI on it.
  OS with desktop
    A good place to begin because you can always connect a display to it to see what is going wrong.
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 61: Ubuntu setup Desktop/Command Line
On the first boot you need to set it up.
Rpi is designed in the United Kingdom, so everything is set for UK.
  Change to USA, select timezone
  SELECT US KEYBOARD!!!!
Create a user, if your team has a standard log in use that.
Select WiFi
It will install updates
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 62: Ubuntu setup SSH
At this point we will do everything from the command line, so we could SSH to the box
Rpis have the SSH server turned off at the start so we need to turn things on.
Open a terminal (command line) window and type ‘sudo raspi-config’
In the interface panel, turn SSH on and I2C on.
Now we can SSH to the box if we know the IP address.
Type ‘ifconfig’ that will tell you the IP address
On you PC open a command line and type ‘ssh stealth@192.168.143.67’
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 63: Ubuntu setup APT
You have just the operating system on the Pi so we need to install packages using the APT tool.
First type ‘sudo apt update’ this checks all of the repositories on the internet for updates to their list of packages.
Things to install
  sudo apt install cmake
  sudo apt install build-essential
  sudo apt install git
  sudo apt install default-jdk
https://github.com/JimWright4089/FIRSTWorkshops
sudo apt install build-essential

## Slide 64: Ubuntu setup SSHFS
So far we have been SSHing to get to the command lines of things.
There is something called SSHFS. Which connects the file system of the Pi to your computer, and it will act like a shared drive.
Google SSHFS and install WinFsp and SHFS-Win.
Now you can map a network drive using \\sshfs\stealth@192.168.143.67
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 65: The Map!
What is the Hardware
Connecting it into a FRC robot
Standalone Things
WPI Raspberry Pi Image
Ubuntu setup
OpenCV/NTCore/Apriltags
I2C comm to 32bit processor
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 66: OpenCV/NTCore/Apriltags git cloning
OpenCV, Apriltags, and NTCore need to be built from source. In order to do this the source code needs to be on your Pi.
Under your home directory (cd ~) make a new directory call FRC. The command is ‘mkdir FRC’. Then change into it ‘cd F’ then hit the tab key then enter. Then clone three things.
git clone https://github.com/opencv/opencv.git
git clone https://github.com/AprilRobotics/apriltag.git
git clone https://github.com/wpilibsuite/allwpilib.git
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 67: OpenCV/NTCore/Apriltags building
Apriltags
  Change into the apriltags directory.
  Make a new directory called build
  In build type ‘cmake ../’, then ‘make’, then ‘sudo make install’
Opencv is basically the same.
  Change into the opencv directory.
  Make a new directory called build
  In build type ‘cmake ../’, then ‘make’, then ‘sudo make install’
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 68: OpenCV/NTCore/Apriltags building
WPIlib
  Change into the WPIlib directory.
  Type ‘./gradlew build
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 69: OpenCV/NTCore/Apriltags Cmake File List
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 70: OpenCV/NTCore/Apriltags Making and Running
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 71: OpenCV/NTCore/Apriltags OpenCV Camera Viewer
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 72: OpenCV/NTCore/Apriltags OpenCV Camera Viewer
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 73: OpenCV/NTCore/Apriltags April Tag Viewer
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 74: OpenCV/NTCore/Apriltags April Tag Viewer
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 75: OpenCV/NTCore/Apriltags April Tag Viewer
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 76: OpenCV/NTCore/Apriltags April Tag Viewer
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 77: OpenCV/NTCore/Apriltags NT Core
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 78: OpenCV/NTCore/Apriltags NT Core
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 79: OpenCV/NTCore/Apriltags NT Core
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 80: OpenCV/NTCore/Apriltags NT Core
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 81: The Map!
What is the Hardware
Connecting it into a FRC robot
Standalone Things
WPI Raspberry Pi Image
Ubuntu setup
OpenCV/NTCore/Apriltags
I2C comm to 32bit processor
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 82: I2C comm to 32bit processor Raspbery Pi Side
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 83: I2C comm to 32bit processor Raspbery Pi Side
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 84: I2C comm to 32bit processor Raspbery Pi Side
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 85: I2C comm to 32bit processor Raspbery Pi Side
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 86: I2C comm to 32bit processor 32bit side
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 87: I2C comm to 32bit processor 32bit side
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 88: I2C comm to 32bit processor 32bit side
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 89: I2C comm to 32bit processor 32bit side
https://jimwright.org/robot/ri3d2020/raspberrypi.html
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 90: The Map!
What is the Hardware
Connecting it into a FRC robot
Standalone Things
WPI Raspberry Pi Image
Ubuntu setup
OpenCV/NTCore/Apriltags
I2C comm to 32bit processor
https://github.com/JimWright4089/FIRSTWorkshops
LAST QUESTIONS

## Slide 91: The Map!
What is the Hardware
Connecting it into a FRC robot
Standalone Things
WPI Raspberry Pi Image
Ubuntu setup
OpenCV/NTCore/Apriltags
I2C comm to 32bit processor
https://github.com/JimWright4089/FIRSTWorkshops
‘Love you all, but go away