## Slide 1: New Sensors! Or Don’t Look at the Lasers!
BUT Don’t panic!
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 2: Intro
Things covered in this class:
  Ports on the Hubs
  Fantastic Beasts Sensors and Where to Find Them
  The I2C Distance Sensor Code.

## Slide 3: Thank you, Dryw Wade
Alumnus FTC Team 8923
Engineer at Sparkfun
CSA at the World Championship.
Wrote the walk through on I2C sensors with FTC

## Slide 4: Hub Sensor Ports
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 5: Digital Sensors
Eight per hub.
These are pulled up.
Connect them to Ground.
3.3V sensors, there is a boost board available if you need 5V.
+3.3V not really needed.
Very fast read

## Slide 6: Analog Sensors
Four per hub.
Measure the amount of voltage into them.
3.3V sensors, there is a boost board available if you need 5V.
On a potentiometer connect +3.3v to one side and Gnd to other.

## Slide 7: UART Ports
These are the most ancient communication ports in the world.
First used in 1959.
Two lines, Transmit and receive, both devices have to be communicating at the same speed called BAUD.
No guaranty the device is listening on the other end.

## Slide 8: RS485 Ports
This was the main communication protocol on an airplane for a long while.
They act like a UART port, but can have multiple devices connected to it.
You will not find any sensors using this.
It’s used for the Hubs talking to each other.

## Slide 9: I2C Ports
This is the most useful port on the Hubs.
Lots of sensors use this.
Dryw has the write up for a temperture sensor here:
https://github.com/FIRST-Tech-Challenge/ftcrobotcontroller/wiki/Writing-an-I2C-Driver

## Slide 10: I2C Ports
All four lines will be used
Clock line
Data line
Each port can handle 127-ish sensors connected to it.
Each Sensor has an address that you have to worry about.
Some sensors allow you to change the address.

## Slide 11: Black and White Line Sensors
Pololu has a good selection of these.
They only sense black and white.
You can use these like a optical limit switch.
Target has to be very close to sensor
Digital ports
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 12: Pololu Digital Distance Sensors
They detect objects at a fixed distance.
5cm, 10cm, 25cm, 50cm, 100cm, 200cm.
If the target is closer than the range they will be a 1.
Farther away is a 0.
Digital ports
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 13: Sharp Distance Sensors
A very old sensor, used in touchless sinks.
This is an analog sensor.
The value larger the longer the target is away from the sensor.
Anything about 4 inches or closer are inverted, so put these 4 inches into the robot.
https://www.sparkfun.com/products/242
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 14: Garmin LIDAR-Lite v4 LED - Distance Measurement Sensor (Qwiic)
A range sensor with a 10m range and 1cm resolution.
I2C sensor that operates at 3.3v.
The address is programable so you can have multiple of these on the same port.
Default port
Qwiic connector, so chaining things is easy.
The sensor code later on uses this.
https://www.sparkfun.com/products/18009
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 15: Adafruit I2C Stemma QT Rotary Encoder Breakout
We have four Encoders on each hub, but what if you need more encoders.
The Encoding is done on this board and you don’t need to do the processing on the hub.
Addresses from 0x36 to 0x3D
Using this is a bit advanced
https://www.adafruit.com/product/4991
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 16: SparkFun Qwiic LED Stick - APA102C
Not a sensor, but useful.
I2C LED strip.
Runs on 3.3V!!!! Power just off the I2C port.
You can chain them to other things on the I2C port.
Address 0x23 or 0x22
https://www.sparkfun.com/products/18354
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 17: SparkFun Qwiic Alphanumeric Display
Also, not a sensor, but useful.
Thank your sponsors while playing!
There is a Red version and a Blue version, if you use the same address you can just swap them out each match.
You can chain them to other things on the I2C port.
Address 0x70, 0x71, 0x72 or 0x73
https://www.sparkfun.com/products/16917
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 18: Explore Sensors
These at only a sample of sensors out there.
Explore these sites for others.
https://www.pololu.com/
https://www.adafruit.com/
https://www.sparkfun.com
https://github.com/JimWright4089/FIRSTWorkshops