## Slide 1: Advanced FTC Code
Don’t panic!
https://github.com/JimWright4089/FIRSTWorkshops

## Slide 2: Intro
Things covered in this class:
  Andriod Studio
  Gyro
  Driving Straight
  Pathfinding

## Slide 3: Andriod Studio
A lot more complicated than OnBoard Java
A lot more flexible as well.
A good tool to know

## Slide 4: Android Studio Setup
Download/Install JDK
Download/Install Android Studio
Get FTC project (next screen)
Import the FTC project.
Hit yes to installing all of the tools and updates Android Studio needs

## Slide 5: FTC Project
Github has it.
https://github.com/ftctechnh/ftc_app
You can download and use it from Github.
Better to fork the code into your Github project. This lets your team check in code,

## Slide 6: Gyro
The gyro on the Rev Expansion Hub is a BNO055IMU. It’s Adafruit’s gyro.
Other gyro major gyro is MPU-9250, it’s Sparkfun’s gyro.
There are trade off. The biggest pro for the BNO is, the code is already written.

## Slide 7: Gyro Setup
BNO055IMU.Parameters parameters = new BNO055IMU.Parameters();
parameters.angleUnit = BNO055IMU.AngleUnit.DEGREES;
parameters.accelUnit=BNO055IMU.AccelUnit.METERS_PERSEC_PERSEC;
parameters.calibrationDataFile = "BNO055IMUCalibration.json";
parameters.loggingEnabled = true;
parameters.loggingTag = "IMU";
parameters.accelerationIntegrationAlgorithm = new JustLoggingAccelerationIntegrator();

## Slide 8: Gyro Setup
imu = hardwareMap.get(BNO055IMU.class, "imu");
imu.initialize(parameters);
imu.startAccelerationIntegration(new Position(), new Velocity(), 1000);

## Slide 9: Gyro get data
telemetry.addAction(new Runnable()
{ @Override public void run()
{
angles = imu.getAngularOrientation(AxesReference.INTRINSIC, AxesOrder.ZYX, AngleUnit.DEGREES); gravity = imu.getGravity();
}
});

## Slide 10: Gyro get data
telemetry.addLine().addData("heading", new Func<String>()
{ @Override public String value() { return formatAngle(angles.angleUnit, angles.firstAngle); }
});

## Slide 11: Driving Straight
FTC robots for the most part drive straight.
The field is not that big.
Gyro is used for Tele/Auto.

## Slide 12: Driving Straight
FTC robots for the most part drive straight.
The field is not that big.
Gyro is used for Tele/Auto.

## Slide 13: Fast and Slow Buttons
double y = driveJoystick.getRawAxis(1); double x = driveJoystick.getRawAxis(2);
x = DriveMath.DeadBand(x,0.05); y = DriveMath.DeadBand(y,0.05);
if (false == driveJoystick.getRawButton(Constants.kFastButton)) {
} else {
if (false == driveJoystick.getRawButton(Constants.kSlowButton)) {
y *= Constants.kNormalSpeed; x *= Constants.kNormalTurnSpeed;
} else {
y *= Constants.kSlowSpeed; x *= Constants.kSlowTurnSpeed;
}
}

## Slide 14: Add the Gyro / Turning
turn = x; speed = y;
mCurrentAngle = angles.firstAngle
if (Math.abs(turn) > 0.2) {
RawDriveRobot(speed*.5, turn*.5);
mTargetAngle = mCurrentAngle;
} else {
* Next page *
}

## Slide 15: Straight and stop
if (Math.abs(speed) > 0.1) {
double angleError = (mTargetAngle - mCurrentAngle);
turnThrottle = angleError * kPgain - (currentAngularRate) * kDgain;
double maxThrot = DriveMath.MaxCorrection(speed, kMaxCorrectionRatio);
turnThrottle = -1*DriveMath.Cap(turnThrottle, maxThrot);
RawDriveRobot(speed,turnThrottle);
}
else
{
RawDriveRobot(0, 0); mTargetAngle = mCurrentAngle;
}

## Slide 16: Raw Drive the Robot
if(mActualSpeed != speed) {
if(mActualSpeed<speed) {
mActualSpeed = Math.min(mActualSpeed+kSpeedGain, speed);
}
else {
mActualSpeed = Math.max(mActualSpeed-kSpeedGain, speed);
} }
double targetSpeedL = (mActualSpeed + turn);
double targetSpeedR = (mActualSpeed - turn);
DriveLF.set(targetSpeedL); DriveRF.set(targetSpeedR);

## Slide 17: Jaci’s Pathfinding
The most populare pathfinding in FRC.
Jaci is on Chiefdelphi’s board all the time.
She loves fixing and making it better.
It may take a lot of work to get it running the way you want.

## Slide 18: Jaci’s Pathfinding
Unfortunately it’s written in C++
I’ve taken the C++ and wrote a tool in Visual Studio to take in a path.csv file an put out a path in java.
It’s in the Github project below.

## Slide 19: Jaci’s Pathfinding
Unfortunately it’s written in C++
I’ve taken the C++ and wrote a tool in Visual Studio to take in a path.csv file an put out a path in java.
The units are what ever you say they are. Feet, Inches, Centimeters, Furlongs, Parsec, or Meters.
Just be constant with the units.

## Slide 20: Jaci’s Path.csv
Name,Desc,Number,X,Y,Theta,X,Y,Theta,X,Y,Theta,X,Y,Theta,X,Y,Theta,X,Y,Theta,X,Y,Theta
Move2,Move two feet,2, 0,0,0, 24,0,0
Red11,Feed Switch from Front Start 1 aud,4, 16,280.25,0,
80,290.25,0,
110,290.25,-30,
128,234,-120

## Slide 21: Jaci’s Settings in the Visual Studio
//----------------------------------------------------------------------------
// Constants
//----------------------------------------------------------------------------
const double TIME_SLICE = 0.02; /sec
const double MAX_VEL = 6.0; /per sec
const double MAX_ACCEL = 10.0;
const double MAX_JERK = 100.0;
const double WHEEL_BASE_WIDTH = 8;

## Slide 22: Jaci’s output
The output is a .java file for every line in the CVS. Subclass of Class.java

## Slide 23: Classes
Path.java
  This is the super class of every path.
public double kSpeed = 14.0;
public int kNumPoints =64;
public double[][] kPoints = new double[][]{
{1.941176, 1.941176, 0.015257, 16.016520, 50.750002, 16.020248, 36.750003},
{3.488871, 4.275835, 0.079671, 16.086297, 50.750060, 16.105765, 36.750074},
The lines are, left speed, right speed, heading, and other the x and y location of the wheels.

## Slide 24: Classes
DrivePathAction.java
  Constructor takes in a Path.
isFinished()
  Checks to see if all the points have been run
end
  Stops the motors
Initialize
  Resets the count to 0
DrivePathAction

## Slide 25: Classes
DrivePathAction.java
execute
  Takes the motors and the gyro and adjusts the speed.
  Should be run every at the speed we said in the settings (0.02 sec)
  Important constant: DIST_TO_REAL_DIST_CONST

## Slide 26: DIST_TO_REAL_DIST_CONST
It takes Jaci’s units and translates them into your robot units.
Make a path that moves 2 feet.
Run that path on your robot, adjusting this const until your robot moves 2 feet.

## Slide 27: Questions
DrivePathAction